## Slide 1: Lab Skills

## Slide 2: Do You Know How to Use a Ruler?
Use a ruler to measure the width of your page
Why do we measure something?

## Slide 3: Measuring Devices
There are two types of measuring devices:
  Analog
  Digital
Analog devices use a scale to give a measurement
  We look where what we are measuring lines up on the scale to take the measurement
Digital devices return a number on a screen
  We read off the number to take the measurement

## Slide 4: Using Analog Measuring Devices
When reading the scale we look to see where what we are looking at lines up with the scale
Most people just look for the closest marking on the scale to take a measurement but you can look in between the markings
  This gives you an additional decimal value!

## Slide 5: Measured Value Versus Actual Value
When we measure something we are never sure that the number we receive is are actual value there is always uncertainty
This uncertainty comes from two sources
  Precision
  Accuracy

## Slide 6: Precision
Reflects how much we know about the measurement
The more digits we have, the more information we have about the measurement
  0.5 versus 0.50
The precision of our instrument limits us from getting the actual value
  Where the digits end in our measurement is the precision of the instrument
  The actual value has digits that go on forever!

## Slide 7: Uncertainty From Precision
When we take a measurement we know the value we are measuring is in between two markings on the scale
Thus somewhere between these markings is the value we are measuring
  We may say the value is closer to one of the markings or in the center
By measuring this way, our uncertainty from the precision of the instrument is half of a marking on the scale

## Slide 8: Accuracy
Completely separate from precision!
Accuracy deals with how well your instrument is calibrated and how well you are using the instrument
Calibration deals the alignment of the scale in the instrument
  Is the scale beat up?
  Has the scale moved, will the scale move during measuring?
Use of the instrument relies on technique
  How well you are holding the measurement
  How you look at the scale

## Slide 9: Parallax
When taking a measurement we typically overlay a scale one what we are measuring
This means there is a distance between the scale and what we are measuring
How we are positioned while looking at affects the measurement we take

## Slide 10: Parallax
Try This!
  Close one eye
  Take both index fingers and hole one in front of the other so the one in front eclipses the one in the rear
  Now move your head and see what happens!
The moving your head affects the alignment of the scale and the point we are aligning to

## Slide 11: Ways to Reduce Parallax
Reduce the distance between the scale and the point we are aligning to
  For a thick meter stick, rotate the stick so the scale is next to the point you are aligning to
Find a reference point to help ensure that you are looking straight on to the scale
  Hooke’s Law Apparatus

## Slide 12: Precision and Accuracy
Precision and accuracy are independent but both limit our measurement
  One of the two will be the limit of our measurement
  We need to decide which one is

## Slide 13: Precision and Accuracy
We quote both precision and accuracy as an interval (plus or minus an amount)
  The width of the interval is the precision or accuracy
Value
+
-
Interval

## Slide 14: Precision and Accuracy
Accuracy is how close we are to the measurement
  This creates an interval around the actual value
  Somewhere in this interval our measurement will lie
The interval created from precision is caused from our inability to read any more values
  The width of the interval is half the width between adjacent markings on the scale

## Slide 15: What This Looks Like
The blue dot will be within the interval around the red dot
+
Measurement
-
Accuracy
Actual Amount
+
-
Precision

## Slide 16: When We Have a Greater Precision
Accuracy limits our measurement
The uncertainty in our measurement is mainly due to the uncertainty in our accuracy
+
Measurement
-
Accuracy
Actual Amount
+
-
Precision

## Slide 17: When We Have a Greater Accuracy
Precision Limits the measurement
The uncertainty of our measurement is mainly due to the uncertainty in our precision
+
Measurement
-
Accuracy
Actual Amount
+
-
Precision

## Slide 18: What you need to know
When using a meter stick you can obtain four digits
You can improve your accuracy by
  Using a meter stick on its edge rather than on its face
  Not measuring from the end of the meter stick (start at the 10 cm mark instead)
The uncertainty for any analog device you will use is half of the smallest measurement on the device
  For a meter stick that is 0.5 mm

## Slide 19: What You Need To Know
When you quote uncertainty you use the ± symbol to denote the range we are uncertain in
We quote our uncertainty to 1 digit
The place value where the uncertainty begins is the place value where our measurement ends
  Ex: 25.21 ± 0.03 cm